## Slide 1: DOE FOR THE CUSTOMER
Chris Vandegrift
V.P. of Engineering
Selas Heat Technology

## Slide 2: 4BZR Regulator
Objective:
Launch the 4BZR – ½” regulator
Conduct performance tests with various conditions: flow rate, pressure variation, washer weights, spring properties and diaphragms.
Meet or exceed the current standard for constant pressure output from the regulator

## Slide 3: 4BZR Before Summer 2013
½” Balanced Zero Regulator
Erratic performance on shut-off
Chart: 4BZR Suction Test @ 14 in-H2O Inlet
| 350 | 300 | 250 | 200 | 150 | 100 | 50 | 25 | 15 | 0
 | 0.1 | 0.02 | -0.12 | -0.22 | -0.23 | -0.2 | -0.1 | 0.09 | 0.2 | 1
 | 0.25 | 0.06 | 0.01 | -0.07 | -0.11 | -0.11 | -0.06 | 0 | 0.03 | 0.25
 | -0.02 | -0.05 | 0.08 | 0.02 | -0.1 | -0.12 | -0.08 | 0.06 | 0.15 | 0.3
 | 0.03 | 0.12 | 0 | -0.07 | -0.1 | -0.07 | 0.01 | 0.33 | 0.4 | 1
 | 0.2 | 0.05 | -0.01 | -0.07 | -0.13 | -0.14 | -0.13 | -0.09 | -0.09 | 0.09
 | 0.18 | 0.1 | -0.05 | -0.08 | -0.13 | -0.15 | -0.13 | -0.06 | -0.04 | 0.1
 | 0.18 | -0.04 | -0.02 | -0.07 | -0.12 | -0.16 | -0.12 | -0.08 | -0.09 | 0.1
 | 0.06 | 0.01 | -0.05 | -0.08 | -0.16 | -0.12 | -0.11 | -0.07 | -0.05 | 0
 | 0.08 | 0.02 | -0.06 | -0.1 | -0.14 | -0.13 | -0.1 | -0.08 | -0.04 | -0.01
 | 0.07 | 0.03 | -0.06 | -0.08 | -0.16 | -0.15 | -0.1 | -0.06 | -0.03 | 0.01
Notes: Best we could do with current setup. out of 20 test showed failure.

## Slide 4: “On-Target with minimum variance.” “Operating with minimum variance is achieved only when a process displays a reasonable degree of statistical control.” -Walter A. Shewhart
Variation

## Slide 5: Virtual Fishbone

## Slide 6: Design of Experiments (DOE)
Design of experiments is a branch of applied statistics that deals with…
  Planning
  Conducting
  Analyzing
  Interpreting
…controlled tests to evaluate the factors that impact the output of the regulator.
Notes: Changing one factor a time is the typical method that we all use to determine which factors have an influence and the intensity of the influence on the output. Sometimes the factors being changed have interactions with one another and DOE will help reveal this. Further, Minitab will generate a mathematical model that can be used to simply choose the desired output and minitab will spit out how the factors should be adjusted to reflect this.

## Slide 7: 4BZR DOE – Main Effects
Main Nut Setting
Seal Nut Setting
Seal Washer
Diameter
Notes: At the end of the DOE, with all other factors fixed or removed due to lack of influence on the outlet pressure, the three remaining main effects were revealed and used in the mathematical model.

## Slide 8: 4BZR After DOE

## Slide 9: 4BZR Response Optimizer
Optimal Settings

## Slide 10: 4BZR Component Recommendation
Seal diaphragm bolt circle | 1.75”
Steel retaining washer I.D. | 1.125”
Steel retaining washer O.D. | 2.0”
Steel retaining washer bolt circle | 1.5”
Cork gasket I.D./O.D./B.C. | Same as steel retaining washer
Seal diaphragm bagging | 0.310”
Seal washer I.D. | 0.203”
Seal washer O.D. | 0.687”
Paper seal gasket washer I.D. | 0.203”
Paper seal gasket washer O.D. | 
Lock washer type | #10 “star” lock washer
Main diaphragm bolt circle | 6.5”
Main diaphragm pan diameter | 3.25”
Seal diaphragm nut setting | 0.649” below top of lower body
Main diaphragm nut setting | 0.068” above top of lower body
Seal diaphragm bolt circle | 1.75”
Steel retaining washer I.D. | 1.125”
Steel retaining washer O.D. | 2.0”
Steel retaining washer bolt circle | 1.5”
Cork gasket I.D./O.D./B.C. | Same as steel retaining washer
Seal diaphragm bagging | 0.310”
Seal washer I.D. | 0.203”
Seal washer O.D. | 0.687”
Paper seal gasket washer I.D. | 0.203”
Paper seal gasket washer O.D. | 
Lock washer type | #10 “star” lock washer
Main diaphragm bolt circle | 6.5”
Main diaphragm pan diameter | 3.25”
Seal diaphragm nut setting | 0.649” below top of lower body
Main diaphragm nut setting | 0.068” above top of lower body
Recommended Components
Modified Assembly Tools

## Slide 11: 4BZR Test Rig
Objective: To test Balanced Zero Regulators performance against quality standards. The ability to digitally record and display test data.

## Slide 12: 4BZR Marketing Claim Tests
Chart: 4BZR Suction Test @ 14 in-H2O Inlet Outlet Pressure vs. Flow Rate
| 350 | 300 | 250 | 200 | 150 | 100 | 50 | 25 | 15 | 0
Before DOEs | 0.175 | 0.04 | -0.055 | -0.145 | -0.17 | -0.155 | -0.08 | 0.045 | 0.115 | 0.625
After DOEs | -0.035 | -0.07 | -0.095 | -0.075 | -0.07 | -0.055 | -0.055 | -0.045 | -0.04 | -0.025

## Slide 13: Thank you!

## Slide 14: Questions?